## Slide 1
Chapter 3 (and Appendix C)
Instruction-Level Parallelism and Its Exploitation
Part 3: Advanced Scheduling
Computer Architecture
A Quantitative Approach, Sixth Edition
“Who’s first?”
“America.”
“Who’s second?”
“Sir, there is no second.”
-Dialog between two observers of the sailing race later named “The America’s Cup” and run every few years -- the inspiration for John Cocke’s naming of the IBM research processor as “America.” This processor was the precursor to the RS/6000 series and the first superscalar microprocessor.

## Slide 2: Acknowledgements
Thanks to many sources for slide material
  © 1990 Morgan Kaufmann Publishers, © 2001-present Elsevier
  Computer Architecture: A Quantitative Approach by J. Hennessy & D. Patterson
  © 1994 Morgan Kaufmann Publishers, © 2001-present Elsevier
  Computer Organization and Design by D. Patterson & J. Hennessy
  © 2002 K. Asinovic & Arvind, MIT
  © 2002 J. Kubiatowicz, University of California at Berkeley
  © 2006, © 2010 No Starch Press for Inside the Machine by J. Stokes
  © 2007 W.-M. Hwu & D. Kirk, University of Illinois & NVIDIA
  © 2007-2010 J. Owens, University of California at Davis
  © 2010 CRC Press for Introduction to Concurrency in Programming Languages by M. Sottile, T. Mattson, and C. Rasmussen
  © 2017, IBM POWER9 Processor Architecture by Sadasivam et al., IBM
  © 2016, © 2019 POWER9 Processor User’s Manual, IBM
  © The OpenPOWER Foundation
  © 2022, W. Feng, Virginia Tech

## Slide 3: Instruction Issue and Completion
Instruction issue—initiate execution
  Instruction lookahead capability—fetch, decode and issue instructions beyond the current instruction
Instruction completion—complete execution
  Processor lookahead capability—complete issued instructions beyond the current instruction
Instruction commit—write back results to the RegFile or D$ (i.e., change the machine state)
Scenarios
  In-order issue w/ in-order completion
  In-order issue w/ out-of-order completion
  Out-of-order issue w/ out-of-order completion & in-order commit
  Out-of-order issue w/ out-of-order completion
Notes: Instruction issue, i.e., when an instruction begins execution phase.
Instruction completion, i.e., when an instruction completes execution.
Because a OOC pipeline allows multiple instructions to be in execution at the same time, it requires multiple functional units, pipelined functional units, or both.

## Slide 4: In-Order Issue, In-Order Completion (IOI-IOC)
Simplest policy is to issue instructions in exact program order and to complete them in the same order they were fetched (i.e., in program order)
Example
  Assume pipelined processor that can fetch & decode 2 instructions per cycle, has 3 functional units (single-cycle adder, a single-cycle shifter, and a two-cycle multiplier), and can complete (and write back) two results per cycle
  Instruction sequence: I1 – needs two execute cycles (a multiply) I2 I3 I4 – needs the same function unit as I3 I5 – needs data value produced by I4 I6 – needs the same function unit as I5
Static Scheduling
Notes: EXAM QUESTION: Modify the pipeline a bit …
Structural and data hazards

## Slide 5: Example: IOI-IOC
EX
IF
ID
WB
I
n
s
t
r.
O
r
d
e
r
I1
I2
I3
I4
I5
I6
EX
IF
ID
WB
EX
EX
WB
EX
WB
EX
IF
ID
WB
EX
IF
ID
WB
IF
ID
IF
ID
I1: two execute cycles
I2
I3
I4: same function unit as I3
I5: data value produced by I4
I6: same function unit as I5
In parallel can
fetch/decode 2
and complete 2
IF
ID
IF
ID
IF
ID
Static Scheduling
Notes: (Why does I2 wait to launch? That’s just the way this pipeline is designed. “Since I have to write back in order, I won’t even start yet.”)
How many cycles to finish? (8)
Where do we have to do a data forward? (EX4-5)
Why can’t I3 issue at time 2? (Two results per cycle.) How about I5+I6, I1+I2, I3+I4?
Limitation of static: Instr issued in order, one instruction that stalls causes entire pipeline to stall, leaving multiple functional units idle.
DIV.D F0, F2, F4; ADD.D F10, F0, F8; SUB.D F12, F8, F14.
SUB.D cannot execute because of dependence of ADD.D on DIV.D causes pipeline to stall.
Turn slide + code fragment above into an EXAM QUESTION.

## Slide 6: In-Order Issue, Out-of-Order Completion
With out-of-order completion, a later instruction may complete before a previous instruction
  Out-of-order completion is used in single-issue pipelined processors to improve the performance of program that has long-latency operations such as divide
When using out-of-order completion, instruction issue is stalled when there is a resource conflict (e.g., for a functional unit) or when the instructions ready to issue need a result that has not yet been computed
Dynamic Scheduling
Notes: EXAM QUESTION: Give an example of IOI-OOC.
DIV.D F0, F2, F4; ADD.D F10, F0, F8; SUB.D F12, F8, F14.
SUB.D cannot execute because of dependence of ADD.D on DIV.D causes pipeline to stall.
Executing SUB.D amounts to checking for two things. Checking for the absence of
Structural hazard
Data hazard

## Slide 7: Example: IOI-OOC
EX
IF
ID
WB
I
n
s
t
r.
O
r
d
e
r
I1
I2
I3
I4
I5
I6
EX
IF
ID
WB
EX
EX
IF
ID
WB
EX
IF
ID
WB
EX
IF
ID
WB
EX
IF
ID
WB
IF
ID
IF
ID
I1: two execute cycles
I2
I3
I4: same function unit as I3
I5: data value produced by I4
I6: same function unit as I5
Dynamic Scheduling
Notes: What has made this faster? (I2 can finish out of order)
How many cycles to finish? (7)
What is the best case time and what is the worst case time for a 6-instruction sequence?
- Best case time: single cycle, no conflicts (shift, add, shift, add, shift, add). 5 cycles total.
- Worst case: multiply, all dependent. 14 cycles total (2*6 + 2 startup)

## Slide 8: Handling Output Dependencies
One more situation that stalls instruction issue w/ IOI-OOC
  I1 – writes to R3 I2 – writes to R3 I5 – reads R3
If the I1 write occurs after the I2 write, then I5 reads an incorrect value for R3
I2 has an output dependency on I1—write after write
The issuing of I2 would have to be stalled if its result might later be overwritten by a previous instruction (i.e., I1) that takes longer to complete—the stall happens before instruction issue
While IOI-OOC yields higher performance, it requires more dependency checking hardware (both write-after-read and write-after-write hazards)
Dynamic Scheduling
Notes: Need arbitration and more ports because there probably are not enough to satisfy all instructions that can complete simultaneously

## Slide 9: Example: IOI-OOC
EX
IF
ID
WB
I
n
s
t
r.
O
r
d
e
r
I1
I2
I3
I4
I5
I6
EX
IF
ID
WB
EX
EX
IF
ID
WB
EX
IF
ID
WB
EX
IF
ID
WB
EX
IF
ID
WB
IF
ID
IF
ID
I1: two execute cycles + WB to R3
I2: WB to R3
I3
I4: same function unit as I3
I5: read R3 + data value produced by I4
I6: same function unit as I5
Dynamic Scheduling
rename
Notes: WAW hazard with I1 and I2.
Address by register renaming, e.g., rename R3 in I2 and I5 to R20, for example.

## Slide 10: Out-of-Order Issue with Out-of-Order Completion (OOI-OOC)
With in-order issue, CPU stops ID when decoded instruction has resource conflict or a data dependency on an issued but uncompleted instruction
  CPU is unable to look beyond conflicted instruction even though more downstream instructions might have no conflicts and thus be issuable
Fetch & decode instructions beyond the conflicted one (“instruction window”: Tetris), store them in an instruction buffer (if room), and flag those instructions in buffer that do NOT have resource conflicts or data dependencies
Flagged instructions are then issued from the buffer w/o regard to their program order  re-order buffer (ROB)
Dynamic Scheduling
Notes: An instruction being in the instruction window only implies that the processor has sufficient information about the instruction to know whether or not it can be issued
Instr window == Tetris

## Slide 11: OOI-OOC Example
EX
IF
ID
WB
I
n
s
t
r.
O
r
d
e
r
I1
I2
I3
I4
I5
I6
EX
IF
ID
WB
EX
EX
IF
ID
WB
EX
IF
ID
WB
EX
IF
ID
WB
EX
IF
ID
WB
I1: two execute cycles
I2
I3
I4: same function unit as I3
I5: data value produced by I4
I6: same function unit as I5
IF
ID
IF
ID
Dynamic Scheduling
Notes: How many cycles? (6)
What’s changed? 6 issues before 5.
What assumption do we need to make when we reorder?
- Assume that I4 is using a different functional unit than I6

## Slide 12: Overview: Dynamic Scheduling
Definition: Rearrange order of instructions to reduce stalls while maintaining data flow
Implications
  Out-of-order execution
  Out-of-order completion
Advantages
  Compiler does NOT need to have knowledge of microarchitecture
  Handles cases where dependencies are unknown at compile time
Disadvantages
  Substantial increase in hardware complexity
  Complicates exception-handling
Creates the possibility for WAR and WAW hazards
Tomasulo’s Algorithm
Notes: Tomasulo’s Approach
  Tracks when operands are available
  Introduces register renaming in hardware
    Minimizes WAW and WAR hazards

## Slide 13: Recap: Dependencies
Each of the three data dependencies …
  True data dependencies (read after write)
  Antidependencies (write after read)
  Output dependencies (write after write)
… manifests itself through the use of registers
(or other storage locations)
True dependencies represent the flow of data and information through a program
Anti- and output dependencies arise because the limited number of registers mean that programmers reuse registers for different computations
storage conflicts
Notes: Storage conflicts, like other resource conflicts can be reduced or eliminated by duplicating the troublesome resource
Formerly last bullet on slide:
When instructions issued out-of-order, correspondence between registers and values breaks down and values conflict for registers

## Slide 14: Recap: Pipeline Scheduling
Statically Scheduled Pipeline
  Fetches an instruction and issues it unless there is a data dependence that cannot be hidden with forwarding.
  Implication: In-order issue; in-order completion
Dynamically Scheduled Pipeline
  Rearranges the order of instructions to reduce stalls while maintaining data flow
  Implication: In-/out-of-order issue; out-of-order completion
Observation
  Commonality: Both must maintain data flow for correctness.
  Difference: Other than static vs. dynamic …
    Static: Minimize stalls by separating dependent instructions
    Dynamic: Minimize stalls by re-arranging instructions based on dynamic presence of dependences
Notes: What’s the diff?
BOTH must abide by the data flow of the program for correctness.

## Slide 15: Example: IOI-OOC
EX
IF
ID
WB
I
n
s
t
r.
O
r
d
e
r
I1
I2
I3
I4
I5
I6
EX
IF
ID
WB
EX
EX
IF
ID
WB
EX
IF
ID
WB
EX
IF
ID
WB
EX
IF
ID
WB
IF
ID
IF
ID
I1: two execute cycles + WB to R3
I2: WB to R3
I3
I4: same function unit as I3
I5: read R3 + data value produced by I4
I6: same function unit as I5
Dynamic Scheduling
rename
Notes: WAW hazard with i1 and i2.
Address by register renaming, e.g., rename R3 in I2 and I5 to R20, for example.

## Slide 16: Dynamic Scheduling with Tomasulo’s Algorithm
Tracks when operands are available (minimize RAW hazards)
Introduces register renaming in hardware
  Addresses WAW & WAR
  hazards
Extends to handle
speculation
  Technique used to reduce
  effect of control dependences
IF precedes ID and fetches into an IR or equivalent (e.g., a queue of pending instructions  re-order buffer). ID has two sub-stages:
  Issue: Decode instruction + check for structural hazards
  Read Operands: Wait until no data hazards
I1: two execute cycles + WB to R3
I2: WB to R3
I3
I4: same function unit as I3
I5: read R3 + data value produced by I4
I6: same function unit as I5
rename
Dynamic Scheduling
Delineate between when instruction begins exect’n
& when it completes execut’n
Notes: WAW & WAR hazards introduced. WAW: output dependence. WAR: anti-dependence.
IF stage precedes the issue stage and may fetch either into an IR or into a queue of pending instructions, e.g., re-order buffer (ROB)
To allow out-of-order execution, ID needs to be split into two sub-stages (implicit before, explicit now to enable "register renaming")
Issue (decode & check for structural hazards)
Read Operands (wait until no data hazards, and THEN read operands)
Distinguish between when an instruction begins execution and when it completes execution. Between then, the instruction is in execution.
Having multiple instructions in execution at the same time requires multiple functional units, pipelined functional units or both.
In an IOI-OOC, all instructions pass through the issue stage in order (“in-order issue”) but can be stalled or bypassed by each other in the second stage (i.e., read operands).
In an OOI-OOC, instructions may pass through the stage out of order.
A technique for allowing instructions to execute out of order when sufficient resources and no data dependences: SCOREBOARDING. (Named after CDC 6600 scoreboard.)
We focus on a more sophisticated technique called Tomasulo’s algorithm, which handles antidependence and output dependence by renaming the registers dynamically.
Tomasulo’s algorithm came from IBM. Goal: Achieve high floating-pt performance.
Issues: IBM’s 360 only had 4 DP floating-pt. units, long floating-point delays, and long memory accesses (on miss).

## Slide 17: Another Example: IOI-OOC Introduces WAR & WAW
Can dynamically schedule with IOI-OOC
  OOC introduces possibility of WAR and WAW hazards, which are NOT issues in a statically scheduled pipeline.
DIV.D F0, F2, F4
ADD.D F6,F0,F8
SUB.D F8,F10,F14
MUL.D F6,F10,F8
How to avoid the above? Register renaming
  Eliminates WAR & WAW hazards by renaming all destination registers, including those with a pending read or write for an earlier instruction, so that the out-of-order write does not affect any instructions that depend on an earlier value of an operand.
Antidependence between ADD.D and SUB.D
If pipeline tries SUB.D before ADD.D, antidependence violated & yields WAR hazard.
Output dependence between ADD.D and MUL.D
If pipeline tries MUL.D before ADD.D, output dependence violated & yields WAW hazard.
Dynamic Scheduling
Notes: PROBLEM
SUB.D cannot execute because of dependence of ADD.D on DIV.D causes pipeline to stall.
YET SUB.D is NOT data dependent on anything in the pipeline
This hazard creates a performance limitation that can be eliminated by not requiring instructions to execute in program order.
In classic 5-stage pipeline, both structural and data hazards can be checked during ID (reason for splitting ID stage into two sub-stages)
To allow SUB.D to execute early, two parts must be satisfied:
Checking for structural hazards
Waiting for absence of data hazards
Antidependence between ADD.D and SUB.D. If pipeline executes SUB.D before ADD.D (which is waiting for the DIV.D), it will violate antidependence, yielding a WAR hazard.
Output dependence between ADD.D and MUL.D. If pipeline executes MUL.D before ADD.D (which is waiting for the DIV.D), it will violate output dependence, yielding a WAW hazard.
OOC creates major complications in handling exceptions. Dynamic scheduling with OOC must preserve exception behavior in the sense that EXACTLY those exceptions that would arise ifthe program were executed in strict program order ACTUALLY do arise.

## Slide 18: Register Renaming
Example
DIV.D F0,F2,F4
ADD.D F6,F0,F8
S.D F6,0(R1)
SUB.D F8,F10,F14
MUL.D F6,F10,F8
antidependence
antidependence
Note: The above code snippet uses the MIPS ISA. The textbook uses the RISC V ISA.
Dynamic Scheduling
output dependence
Identify all the data hazards for an IOC pipeline.
Identify all the data hazards for an OOC pipeline.
Two antidependences (WAR) and an output dependence (WAW)
Notes: Two antidependences and an output dependence (F6)
EXAM QUESTION: (1) Identify all the data hazards for a IOC pipeline. (2) Identify all the hazards for a OOC pipeline.
RAW (3): DIV.D and ADD.D; SUB.D and MUL.D, and ADD.D and S.D.
WAR (2): Use of F8 by ADD.D and use of F6 by SUB.D.
WAW (1): ADD.D may finish later than the MUL.D.
WAR and WAW dependences can be eliminated by register renaming.

## Slide 19: Register Renaming
Example
DIV.D F0,F2,F4
ADD.D S,F0,F8
S.D S,0(R1)
SUB.D T,F10,F14
MUL.D F6,F10,T
Now only RAW hazards remain, which can be strictly ordered
Any subsequent uses of F8 must be replaced by the register T
Note: The above code snippet uses the MIPS ISA. The textbook uses the RISC V ISA.
Dynamic Scheduling
DIV.D F0,F2,F4
ADD.D F6,F0,F8
S.D F6,0(R1)
SUB.D F8,F10,F14
MUL.D F6,F10,F8
Notes: Assume the existence of two temporary registers, S and T. WAW and WAR hazards are now gone.
Could this renaming process have occurred at compile time? Y.
CAUTION: Any subsequent uses of F8 must be replaced by the register T.
Finding any uses of F8 that are later in the code requires sophisticated compiler or hardware support since there may be intervening branches between above code and a later use of F8.
Tomasulo’s algorithm can handle renaming across branches.

## Slide 20: Register Renaming
Tomasulo’s Approach
  Tracks when operands are available
  Introduces register renaming in hardware
  via reservation stations (RS)
    Minimizes WAW and WAR hazards (by renaming destination regs)
Register renaming is provided by reservation stations (RS)
  Contains:
    The instruction
    Buffered operand values (when available)
    Reservation station number of instruction providing the operand values
Dynamic Scheduling

## Slide 21: Register Renaming
Dynamic Scheduling
Register renaming provided by reservation stations (RS)
  RS fetches and buffers an operand as soon as it becomes available, eliminating the need to get the operand from a register
  Pending instructions designate the RS to which they will send their output
    Result values broadcast on a result bus called common data bus (CDB)
  Only the last output updates the register file
Observations
  As instructions are issued, the register specifiers are renamed with the reservation station
  May be more reservation stations than registers
  Load and store buffers
    Contain data and addresses, act like
    reservation stations
Notes: RS buffers the operands of instructions waiting to issue.
Basic idea: RS fetches and buffers an operand as soon as available, eliminating the need to get the operand from a register. (This is the renaming but done in HW.)
Pending instructions designate the RS that will provide their input.
When successive writes to a register overlap in execution, only the last one is actually used to update the register. (See code fragment again).
Better performance, but the tradeoff is … more complexity and more power consumption.
Solution: Let the compiler do it. See previous slide. What are S and T? They ultimately have to be actual registers. Problem? Limited registers.
Hence, Tomasulo’s algorithm in hardware.
- Generally more RS than real registers  can eliminate more hazards arising from name dependences.

## Slide 22: High-Level Architecture for Tomasulo’s Algorithm
Register renaming via
reservation stations (RS)
Load and store buffers
  Contain data & addresses,
  act like reservation stations
Advantages
  Distribution of hazard
  detection logic
  Elimination of stalls for
  WAW and WAR hazards
  by renaming all destination
  registers
No execution tables shown.
Dynamic Scheduling
Notes: Register renaming eliminates WAR and WAW hazards by renaming all destination registers, including those with a pending read or write for an earlier instruction.
Register renaming is provided by reservation stations (RS)
  Contains:
    The instruction
    Buffered operand values (when available)
    Reservation station number of instruction providing the operand values
Advantages:
Hazard detection and execution control are distributed.
Info held in RS at each functional unit determines when an instruction can being execution at that unit.
Results are passed directly to functional units from RS where they are buffered, rather than going through registers. (This bypassing is done with a common result bus that allows all units waiting for an operand to be loaded simultaneously.
Each RS holds an inst that has been issued and is awaiting execution at a functional unit (structural hazard) and either operand values (data hazard), if already computed or names of RS that will provide operand values.
(In pipelines with multiple execution units AND issuing multiple instructions per clock, more than one results bus will be needed.)

## Slide 23: Tomasulo’s Algorithm at High Level
Three steps that an instruction goes through …
  Issue (or Dispatch), where register renaming occurs
    Get next instruction from FIFO queue
    If available RS, issue instruction to RS w/ operand values, if available. If operand values not available, stall instruction in RS and keep track of the functional units that will produce operand values.
    If no available RS, structural hazard  stall until RS or buffer free …
  Execute
    When operand available (via CDB), store it in any RS waiting for it
    When all operands ready (i.e., no RAW hazard), issue instruction
    Loads & store maintained in program order via effective address calc.
    No instruction allowed to initiate execution until all branches that precede it in program order have completed (to preserve exception behavior)
  Write result
    Write result on CDB into registers and RS (including store buffers)
      (Stores must wait until address and value are received)
Dynamic Scheduling
Notes: First step is actually an IF (instruction fetch).
ISSUE
FIFO order: Ensures maintenance of correct data flow.
No available RS? Structural hazard. How many FP adders and FP multipliers in previous diagram? 3 and 2.
If operands are NOT in registers, keep track of the functional units that will produce the operands. This step renames registers, eliminating WAR and WAW hazards.
EXECUTE
If one or more of the operands is not yet available, monitor the CDB for it. When operand available, …
By delaying instruction execution until operands are available, RAW hazards are avoided.
When multiple instructions become ready in the same clock cycle for the same functional unit, the unit chooses among them. (L.D. and S.D are trickier. See below.)
L.D in load buffer execute as soon as memory unit available.
S.D in store buffer MUST wait for value to be stored in buffer before sending to memory unit.
L.D and S.D are maintained in program order through the effective address calculation, thus preventing hazard via memory.
To preserve exception behavior, no instruction is allowed to initiate execution until a branch that precedes the instruction in program order has completed. This restriction guarantees that an instruction that causes an exception during execution really would have executed.
All this means is that in a CPU with branch prediction, the CPU must know that the branch prediction is correct BEFORE allowing an instruction AFTER the branch to begin execution.
WRITE RESULT
When result is available, write onto CDB and into registers and into any reservation stations, including store buffers.
The data structures and associated tags that detect and eliminate hazards are attached to the (1) RS, (2) reg file, and (3) load & store buffers.

## Slide 24: High-Level Architecture for Tomasulo’s Algorithm
Each RS has seven fields:
Op
  Op to do on src operands
Qj, Qk
  RS that produce corresponding src operand
  (Zero value means src operand in Vj or Vk or not needed)
Vj, Vk
  Value of src operands
  (Only one V field or Q field valid for each operand)
A
  Holds info for memory addr calc
Busy
  Indicates RS and associated functional unit are busy
Notes: The data structures and associated tags that detect and eliminate hazards are attached to the (1) RS, (2) reg file, and (3) load & store buffers.
The tags are effectively NAMES for an extended set of virtual registers used for renaming. In OUR example (see next slide briefly),
Tag field is a 4-bit quantity denoting 1 of 5 RS or 1 of 5 load buffers  Equivalent of 10 (virtual) registers that can be designated as result registers (vs. the 4 DP registers in the IBM 360 mainframe). In a CPU with more real registers (e.g., 32), want renaming to provide an even larger set of virtual registers, i.e., HUNDREDS.
Tag field indicates the RS containing the instruction that will produce a result needed as a source operand.
ONCE an instruction has issued and is waiting for a source operand, it refers to the operand by the RS # (NOT the register number).
So, WAW and WAR hazards are eliminated by renaming results using RS #s, one of the two noted advantages. What was the other?
Distribution of hazard detection logic. In statically scheduled pipeline, e.g., MIPS32 ISA, forwarding & bypassing centralized in HW. Here it is distributed.
 Combination of the CDB and the retrieval of results from the CDB by the RS implements forwarding & bypassing.
Each RS has 7 fields. Switch back and forth between this slide and next.
Op: Source operands S1 and S2.
Qj, Qk: RS that will produce the corresponding source operand; a value of 0 indicates that the source operand is already in Vj, Vk or is not needed.
Vj, Vk: For loads, the Vk field is used to hold the offset field.
A: Holds info for memory address calc for a L.D or S.D. Initially immediate field of instruction stored; after address calc, effective address stored.
The register file has a field, Qi:
Qi: # of the reservation station that contains the operation whose results should be stored into this register.
(If Qi is blank or zero, no active instruction is computing a result destined for this register.
The load and store buffers each have a field, A:
A: Holds result of effective address.

## Slide 25: Example: Tomasulo’s in Action
Note: The above code snippet uses the MIPS ISA. The textbook uses the RISC V ISA.
Dynamic Scheduling
Assume the following execute latencies:
L.D 1 cycle
ADD.D 2 cycles
MUL.D 6 cycles
DIV.D 12 cycles
What do the status tables look like when MUL.D is ready to write its result?
Let’s find out!
Notes: Orientation:
# appended to names Add, Mult, and Load stand for the tag for that RS. NOT actually part of hardware; included here to help understanding. In hardware, RS keeps state of each operation that has issued.
Hazard detection and execution control are distributed. Results are passed directly to functional units from RS, where they are buffered rather going through registers.
Reservation stations & register tags shown when all instructions have issued but only first L.D has completed and written its result to the CDB.
Second L.D has completed effective address calculation but waiting on the memory unit.
Use the array Regs[ ] to refer to the register file and the array Mem[ ] to refer to the memory
An operand is specified by either a Q field or a V field at any time.
Notice ADD.D instruction, which has a WAR hazard at the WB stage, has issued and could complete before DIV.D initiates.
Elimination of WAW and WAR hazards. See the DIV.D and ADD.D just discussed.
WAR hazard involving F6
Eliminated via register renaming to RS.
  If instr providing value for DIV has completed, then Vk will store the result (rather than F6 storing the result), allowing DIV.D to execute independent of ADD.D. THIS IS THE CASE THAT IS SHOWN with Load1.
  If first L.D instruction, which writes to F6, did NOT complete, then Qk would point to the Load1 RS.
Thus, in either case, ADD.D can issue and begin executing as the register renaming has resolved the WAR hazard.
That is, any uses of the result of the DIV.D will point to the RS, allowing ADD.D to complete and store its values into the registers without affecting the DIV.D

## Slide 26: Example: Tomasulo’s for IOI/OOI-OOC
I
n
s
t
r.
O
r
d
e
r
I1
I2
I3
I4
I5
I6
EX
IF
ID
WB
EX
IF
ID
IF
ID
IF
ID
EX
EX
EX
EX
EX
EX
IF
ID
IF
ID
IF
ID
IF
ID
IF
ID
IF
ID
IF
ID
IF
ID
Notes: What would the likely latencies be in this case? Assuming a single-issue pipeline.
What about assuming a dual-issue pipeline?

## Slide 27: Tomasulo’s w/ Straightline Code
Note: The above code snippet uses the MIPS ISA. The textbook uses the RISC V ISA.
Dynamic Scheduling
Assume the following execute latencies:
L.D 1 cycle
ADD.D 2 cycles
MUL.D 6 cycles
DIV.D 12 cycles
What do the status tables look like when MUL.D is ready to write its result?
Notes: ADD.D has completed because the operands of DIV.D were copied (renamed), thus overcoming the WAR hazard.
See next (hidden) slide for details.

## Slide 28
L.D F6,32(R2)
L.D F2,44(R3)
MUL.D F0,F2,F4
SUB.D F8,F2,F6
DIV.D F10,F0,F6
ADD.D F6,F8,F2
R3
F4
R2

## Slide 29: Example: Tomasulo’s for IOI/OOI-OOC
I
n
s
t
r.
O
r
d
e
r
I1
I2
I3
I4
I5
I6
Notes: Homework problem!
Assume a single-issue pipeline.
Assume a dual-issue pipeline.

## Slide 30: Tomasulo’s with Loop-Based Code
RISC-V Loop-Based Code
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x1 != x2
Assumption
Predict branches taken.
Implication: RS allow multiple executions of the loop to run simultaneously, an advantage gained WITHOUT changing the code. Loop is unrolled dynamically by hardware using the RS obtained by “register renaming.” (Ignore integer ALU operation for now as branch is predicted as taken.)
Dynamic Scheduling
Notes: This loop merely multiplies the elements of an array by a scalar in f2.
Observations:
Once system is executing two iterations, CPI ~ 1.0 if multiplies can execute in 4 cycles.
If multiplies take 6 cycles, then additional iterations will be needed before the steady state can be reached. This requires more RS to hold instructions that are in execution.

## Slide 31: Tomasulo’s with Loop-Based Code
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x1 != x2
Observations
A load (fld) and a store (fsd) can be safely done out of order iff they access different locations, but what if they access the same?
  Load is before store in program order & interchanging them  WAR hazard
  Store is before load in program order & interchanging them  RAW hazard
  Also, interchanging two stores  WAW hazard
How to Detect Hazards on Loads & Stores?
Dynamic Scheduling
Notes: To understand the full power of eliminating WAW and WAR hazards via dynamic renaming of registers, let’s look at a loop.
 means “results in” here
WAR Hazard: To determine if a load can be executed, CPU checks if any uncompleted stores that precedes the load in program order share the same data memory address as the load. (See earlier figure with ROB.)
RAW & WAW Hazard: Similarly, a store must wait until there are no unexecuted loads or stores that are earlier in program order that share the same data memory address.

## Slide 32: Tomasulo’s with Loop-Based Code
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x1 != x2
How to Detect Hazards on Loads & Stores?
Loads
  Compute the data memory address associated with any earlier memory operation  pragmatically check the “A” field of all active (store) buffers
  If load address matches address of any active entry in store buffer, load is not sent to load buffer until conflicting store completes (i.e., respect RAW hazard)
Stores
  Similar to loads except that CPU must check for conflicts on both the load buffers AND store buffers (since conflicting stores cannot be reordered with respect to either a load or a store, i.e., WAR or WAW).
Dynamic Scheduling
Notes: To understand the full power of eliminating WAW and WAR hazards via dynamic renaming of registers, let’s look at a loop.
 means “results in” here
WAR Hazard: To determine if a load can be executed, CPU checks if any uncompleted stores that precedes the load in program order share the same data memory address as the load. (See earlier figure with ROB.)
RAW & WAW Hazard: Similarly, a store must wait until there are no unexecuted loads or stores that are earlier in program order that share the same data memory address.

## Slide 33: Tomasulo’s with Loop-Based Code
VLIW approach later
Dynamic Scheduling
Notes: Convince yourself that the RAW, WAR, and WAW hazards on loads and stores is handled in this example.

## Slide 34: Adoption of Tomasulo’s Algorithm
Proposed in 1967! 😳
Not widely adopted until … the 1990s!
  Intro of caches created unpredictable delays  need for dynamic scheduling
    Out-of-order execution (and completion) allows CPU to continue executing instructions while waiting the completion of a cache miss, thus hiding all or part of the cache-miss penalty.
      What kind of advanced cache optimization is this?
  CPUs became more aggressive about their issue capability while CPU designers concerned with the performance of difficult-to-schedule code (e.g., non-numeric code  graphs)  need for automated register renaming, dynamic scheduling, and speculation (coming up next)
  Can achieve higher performance without the compiler needing to target code to a specific pipeline structure (i.e., architecture)
Dynamic Scheduling
Notes: What kind of advanced cache optimization is this? Non-blocking $

## Slide 35: Recap: Dynamic Scheduling
Dynamic scheduling implies
  Out-of-order execution
  Out-of-order completion
Creates the possibility for WAR and WAW hazards
Tomasulo’s Approach
  Tracks when operands are available
  Introduces register renaming in hardware
    Minimizes WAW and WAR hazards
Dynamic Scheduling
Notes: Tomasulo’s WITHOUT speculation thus far.

## Slide 36: Hardware-Based Speculation
Execute instructions along predicted execution paths but only commit the results if prediction was correct
Instruction commit
  Allow an instruction to update the register file when instruction is no longer speculative
Need an additional piece of hardware to prevent any irrevocable action until an instruction commits
  i.e., updating state or taking an execution
Dynamic Scheduling & Hardware-based Speculation

## Slide 37: Hardware-Based Speculation
Dynamic Scheduling vs. (Hardware-Based) Speculation
Dynamic Scheduling
  Fetch, decode, and issue instructions
Speculation
  Fetch, decode, issue, and execute instructions
Key Ideas Behind Hardware-Based Speculation
  Dynamic branch prediction
    Choose which instructions to execute
  Speculation
    Execute instructions before control dependences are resolved
  Dynamic scheduling
    Deal with the scheduling of different combinations of basic blocks

## Slide 38: Re-order Buffer (ROB)
Re-order buffer
  Holds the result of instruction between completion and commit
Four fields
  Instruction type: branch/store/register
  Destination field: register number
  Value field: output value
  Ready field: completed execution?
Modify reservation stations
  Operand source is now reorder buffer instead of functional unit
Dynamic Scheduling & Hardware-based Speculation
Notes: Why is the operand source now the reorder buffer instead of functional unit?
Recall: Execute instructions along predicted execution paths but only commit the results if prediction was correct.
This means we need a place *after* EXE to hold speculative results (across a branch) before we commit to register file.

## Slide 39: Tomasulo’s with Reorder Buffer
Dynamic Scheduling & Hardware-based Speculation
Notes: We’ll first show how the ROB impacts the previous code example, i.e., no loop.
Talking about what but not how this works …

## Slide 40: Reorder Buffer
Issue
  Allocate RS and ROB; read available operands
Execute
  Begin execution when operand values are available
Write result
  Write result and ROB tag on CDB
Commit
  When ROB reaches head of ROB, update register
  When a mispredicted branch reaches head of ROB, discard all entries
Dynamic Scheduling & Hardware-based Speculation

## Slide 41: Re-order Buffer (ROB)
Register values and memory values are not written until an instruction commits
On misprediction
  Speculated entries in reorder buffer (ROB) are cleared
Exceptions
  Not recognized until it is ready to commit
Hardware-based Speculation

## Slide 42: Tomasulo’s with Reorder Buffer
Dynamic Scheduling & Hardware-based Speculation
Notes: We’ll first show how the ROB impacts the previous code example, i.e., no loop.
Talking about what but not how this works …

## Slide 43: ROB w/ Previous Straightline Code (no loop)
L.D F6,32(R2)
L.D F2,44(R3)
MUL.D F0,F2,F4
SUB.D F8,F2,F6
DIV.D F10,F0,F6
ADD.D F6,F8,F2
R2
R3
F6
F2
F0
F8
F10*
F6
R2
R3
MUL
DIV
Dynamic Scheduling & Hardware-based Speculation
Notes: F10* is correct. F0 in (old) textbook incorrect.

## Slide 44: ROB with Loop-Based Code
MIPS Loop-Based Code
Loop: L.D F0,0(R1)
MUL.D F4,F0,F2
S.D F4,0(R1)
ADDI R1,R1,#8
BNE R1,R2,Loop // branches if R1 != R2
RISC-V Loop-Based Code
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x1 != x2
Dynamic Scheduling & Hardware-based Speculation
Notes: To understand the full power of eliminating WAW and WAR hazards via dynamic renaming of registers, let’s look at a loop.

## Slide 45: ROB with Loop-Based Code
RISC-V Loop-Based Code
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x1 != x2
Assumption
Predict branches taken.
Implication: RS allow multiple executions of the loop to run simultaneously, an advantage gained WITHOUT changing the code. Loop is unrolled dynamically by hardware using the RS obtained by “register renaming.” (Ignore integer ALU operation for now as branch is predicted as taken.)
Dynamic Scheduling & Hardware-based Speculation
Notes: This loop merely multiplies the elements of an array by a scalar in f2.
Observations:
Once system is executing two iterations, CPI ~ 1.0 if multiplies can execute in 4 cycles.
If multiplies take 6 cycles, then additional iterations will be needed before the steady state can be reached. This requires more RS to hold instructions that are in execution.

## Slide 46: ROB with Loop-Based Code
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x1 != x2
Observations
A load (fld) and a store (fsd) can be safely done out of order iff they access different locations, but what if they access the same?
  Load is before store in program order & interchanging them  WAR hazard
  Store is before load in program order & interchanging them  RAW hazard
  Also, interchanging two stores  WAW hazard
How to Detect Hazards on Loads & Stores?
Dynamic Scheduling & Hardware-based Speculation
Notes: To understand the full power of eliminating WAW and WAR hazards via dynamic renaming of registers, let’s look at a loop.
 means “results in” here
WAR Hazard: To determine if a load can be executed, CPU checks if any uncompleted stores that precedes the load in program order share the same data memory address as the load. (See earlier figure with ROB.)
RAW & WAW Hazard: Similarly, a store must wait until there are no unexecuted loads or stores that are earlier in program order that share the same data memory address.

## Slide 47: ROB with Loop-Based Code
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x1 != x2
How to Detect Hazards on Loads & Stores?
Loads
  Compute the data memory address associated with any earlier memory operation  pragmatically check the “A” field of all active (store) buffers
  If load address matches address of any active entry in store buffer, load is not sent to load buffer until conflicting store completes (i.e., respect RAW hazard)
Stores
  Similar to loads except that CPU must check for conflicts on both the load buffers AND store buffers (since conflicting stores cannot be reordered with respect to either a load or a store, i.e., WAR or WAW).
Dynamic Scheduling & Hardware-based Speculation
Notes: To understand the full power of eliminating WAW and WAR hazards via dynamic renaming of registers, let’s look at a loop.
 means “results in” here
WAR Hazard: To determine if a load can be executed, CPU checks if any uncompleted stores that precedes the load in program order share the same data memory address as the load. (See earlier figure with ROB.)
RAW & WAW Hazard: Similarly, a store must wait until there are no unexecuted loads or stores that are earlier in program order that share the same data memory address.

## Slide 48: ROB with Loop-Based Code
Dynamic Scheduling & Hardware-based Speculation
Tomasulo’s
Algorithm
VLIW approach later
Notes: Convince yourself that the RAW, WAR, and WAW hazards on loads and stores is handled in this example.

## Slide 49: Adoption of Tomasulo’s
Proposed in 1967! 😳
Not widely adopted until … the 1990s!
  Intro of caches created unpredictable delays  need for dynamic scheduling
    Out-of-order execution (and completion) allows CPU to continue executing instructions while waiting the completion of a cache miss, thus hiding all or part of the cache-miss penalty.
      What kind of advanced cache optimization is this?
  CPUs became more aggressive about their issue capability while CPU designers concerned with the performance of difficult-to-schedule code (e.g., non-numeric code  graphs)  need for automated register renaming, dynamic scheduling, and speculation (coming up next)
  Can achieve higher performance without the compiler needing to target code to a specific pipeline structure (i.e., architecture)
Dynamic Scheduling & Hardware-based Speculation
Notes: Non-blocking $

## Slide 50: ROB with Loop-Based Code
MIPS Loop-Based Code
Loop: L.D R2,0(R1) // R2 = array element
ADDI R2,R2,#1 // increment R2
S.D R2,0(R1) // store result
ADDI R1,R1,#8 // increment ptr to next elt
BNE R2,R3,Loop // branch if not last
RISC-V Loop-Based Code
Loop: ld x2,0(x1) // x2=array element
addi x2,x2,1 // increment x2
sd x2,0(x1) // store result
addi x1,x1,8 // increment pointer
bne x2,x3,Loop // branch if not last
Dynamic Scheduling, Multiple Issue, and Speculation
Notes: To understand the full power of eliminating WAW and WAR hazards via dynamic renaming of registers, let’s look at a loop.
This loop merely increments each element of an array.

## Slide 51: ROB with Loop-Based Code
RISC-V Loop-Based Code
Loop: ld x2,0(x1) // x2=array element
addi x2,x2,1 // increment x2
sd x2,0(x1) // store result
addi x1,x1,8 // increment pointer
bne x2,x3,Loop // branch if not last
Assumptions
Predict branches taken.
Implication: RS allow multiple executions of the loop to run simultaneously, an advantage gained WITHOUT changing the code. Loop is unrolled dynamically by hardware using the RS obtained by “register renaming.”
Dynamic Scheduling, Multiple Issue, and Speculation
Notes: BEFORE: For loop unrolling, register renaming at compile time and using real registers, which, in turn, causes register pressure.
Now: For loop unrolling, register renaming at run time using RS (“virtual registers”)

## Slide 52: ROB Example (No Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation
Notes: Is this a single- or multiple-issue pipeline? If multiple, how many way-multiple? 2-way

## Slide 53: ROB Example (with Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 54: Recall: Hardware-Based Speculation
Execute instructions along predicted execution paths but only commit the results if prediction was correct
Instruction commit
  Allow an instruction to update the register file when instruction is no longer speculative
Need an additional piece of hardware to prevent any irrevocable action until an instruction commits
  i.e., updating state or taking an execution
Dynamic Scheduling & Hardware-based Speculation
Notes: Exploiting more instruction-level parallelism (ILP) requires that we overcome the limitations of control dependences.
How?
Speculate on the outcome of branches
Execute the program as if our predictions are correct
How is this similar to the dynamic scheduling (via Tomasulo’s algorithm) that we have been talking about?
Dynamic scheduling: Fetches, decodes, and issues instructions.
Speculation: Fetches, decodes, issues, and EXECUTES instructions, as if our branch predictions are always correct.
In this class, we only talked about hardware-based speculation (via re-order buffer or ROB).
Appendix H discusses ways to support speculation by the compiler.

## Slide 55: Recall: Hardware-Based Speculation
Dynamic Scheduling vs. (Hardware-Based) Speculation
Dynamic Scheduling
  Fetch, decode, and issue instructions
Speculation
  Fetch, decode, issue, and execute instructions
Key Ideas Behind Hardware-Based Speculation
  Dynamic branch prediction
    Choose which instructions to execute
  Speculation
    Execute instructions before control dependences are resolved
  Dynamic scheduling
    Deal with the scheduling of different combinations of basic blocks

## Slide 56: Dynamic, Multiple Issue, and Speculation
Modern Microarchitectures
  Dynamic scheduling + multiple issue + speculation
Approaches
  Assign reservation stations and update pipeline control table in half clock cycles
    Only supports 2 instructions/clock
  Design logic to handle any possible dependencies between the instructions
  Hybrid approaches
Issue logic is the bottleneck in dynamically-scheduled superscalar processors
Dynamic Scheduling & Multiple Issue
Notes: Dynamic scheduling: Fetches, decodes, and issues instructions.
Speculation: Fetches, decodes, issues, and EXECUTES instructions, as if our branch predictions are always correct.
ISSUE logic is the bottleneck, not fetch and decode logic

## Slide 57: Multiple Issue
Limit the number of instructions of a given class that can be issued in a “bundle” (to simplify RS allocation)
  Example: one FP, one integer, one load, one store
Examine all the dependencies between the instructions in the bundle
If dependencies exist in bundle, encode them in reservation stations
Need multiple completion/commit
Dynamic Scheduling
Dynamic Scheduling & Multiple Issue
Notes: What does “encoding them in reservation stations” mean?

## Slide 58: Re-visiting Re-order Buffer
Dynamic Scheduling
Dynamic Scheduling & Multiple Issue
Notes: Talking about what but not how this works …

## Slide 59: Example
Loop: LD R2,0(R1) ; R2=array element
DADDIU R2,R2,#1 ; increment R2
SD R2,0(R1) ; store result
DADDIU R1,R1,#8 ; increment pointer
BNE R2,R3,LOOP ; branch if not last element
Assumptions
Predict branches taken
Implication: RS allow multiple executions of the loop to run simultaneously, an advantage gained WITHOUT changing the code. Loop is unrolled dynamically by hardware using the RS obtained by “register renaming.”
Dynamic Scheduling
Dynamic Scheduling & Multiple Issue
Notes: Loop increments each element of an integer array on a two-issue processor.

## Slide 60: Example (No Speculation)
Dynamic Scheduling
Dynamic Scheduling & Multiple Issue
Notes: Assume separate integer functional units for effective address calculation, for ALU operations, and for branch condition evaluation.
Assume that up to two instructions of any type can commit per clock.
Third branch executes in clock cycle 19 on the nonspeculative pipeline.
Third branch executes in clock cycle 13 on the speculative processor.
Because the completion rate on the nonspeculative pipeline is falling behind the issue rate rapidly, the nonspeculative pipeline will stall when a few more iterations are issued.
The performance of the nonspeculative processor can be improved by allowing load instructions to complete effective address calculation before a branch is decided, but unless speculative memory accesses are allowed, this improvement will gain only 1 clock per iteration.

## Slide 61: Example (Speculation)
Dynamic Scheduling & Multiple Issue
Notes: LD following the BNE can start execution early because it is speculative.

## Slide 62: Speculation: How Much?
How much to speculate
  Mis-speculation degrades performance and power relative to no speculation
    May cause additional misses (cache, TLB)
  Prevent speculative code from causing higher costing misses (e.g., L2)
Speculating through multiple branches
  Complicates speculation recovery
  No processor can resolve multiple branches per cycle
Energy efficiency
  Speculation is only energy efficient when it significantly improves performance
Adv. Techniques for Instruction Delivery and Speculation

## Slide 63: How Much?
Adv. Techniques for Instruction Delivery and Speculation
integer

## Slide 64: Energy Efficiency
Speculation and energy efficiency
  Speculation is only energy-efficient when it significantly improves performance
Value prediction
  Uses:
    Loads that load from a constant pool
    Instruction that produces a value from a small set of values
  Not been incorporated into modern processors
  Similar idea--address aliasing prediction--is used on some processors
Adv. Techniques for Instruction Delivery and Speculation

## Slide 65: Recap
What is instruction-level parallelism (ILP)?
  A measure of how many of the operations in a computer program can be performed simultaneously.
  Pipelining  universal technique in 1985
    Overlaps execution of instructions  exploits ILP
How do processors extract ILP to get faster?
  More parallelism (or more work per pipeline stage): fewer clocks/instruction [more instructions/cycle]
    Get WIDER
  Deeper pipeline stages: fewer gates/clock
    Get DEEPER
  Transistors get faster (Moore’s Law): fewer ps/gate
    Get FASTER
What do processors do to extract ILP?
ILP
Notes: How do processors extract ILP? That is, why do processors get faster?
Does a faster processor mean a faster computer? Why? Why not?
- Remember last chapter? Memory hierarchy.

## Slide 66: Get WIDER: Multiple Issue
To achieve CPI < 1, need to complete multiple instructions per clock
Solutions
  Dynamically scheduled superscalar processors
  Statically scheduled superscalar processors
  VLIW (very long instruction word) processors
ILP

## Slide 67: Get WIDER: Machine Parallelism
Two approaches for machine parallelism, where the responsibility of resolving hazards is …
  Hardware-based dynamic approaches
    Dynamic-issue superscalar
    Typically used in server and desktop processors
    Not used as extensively in PMP processors
  Software-based static approaches (i.e., compiler)
    Static “VLIW: Very Long Instruction Word”
    Not as successful outside of scientific applications
Notes: How do processors extract ILP? That is, why do processors get faster?
Does a faster processor mean a faster computer? Why? Why not?
- Remember last chapter? Memory hierarchy.

## Slide 68: Multiple-Issue Processor Styles
Dynamic multiple-issue processors (aka superscalar)
  Decisions on which instructions to execute simultaneously are being made dynamically (at run time by the hardware)
    Example: IBM Power 2, Pentium Pro/2/3/4, Core, MIPS R10K, HP PA 8500
Static multiple-issue processors (aka VLIW)
  Decisions on which instructions to execute simultaneously are being made statically (at compile time by the compiler)
    Example: Intel Itanium and Itanium 2 for the IA-64 ISA—EPIC (Explicit Parallel Instruction Computer)

## Slide 69: Multiple-Issue Processor Styles
Dynamic Scheduling
Notes: Dynamic scheduling implies:
  Out-of-order execution
  Out-of-order completion
Which of these architectures is the simplest in hardware?
Which of these architectures is the most complex in hardware?

## Slide 70: Multiple-Issue Processor Styles
Dynamic multiple-issue processors (aka superscalar)
  Decisions on which instructions to execute simultaneously are being made dynamically (at run time by the hardware)
    Example: IBM Power 2, Pentium Pro/2/3/4, Core, MIPS R10K, HP PA 8500
Static multiple-issue processors (aka VLIW)
  Decisions on which instructions to execute simultaneously are being made statically (at compile time by the compiler)
    Example: Intel Itanium and Itanium 2 for the IA-64 ISA—EPIC (Explicit Parallel Instruction Computer)

## Slide 71: VLIW Beginnings
VLIW: Very Long Instruction Word
Led to a startup (MultiFlow) whose computers worked, but which went out of business ... the ideas remain influential.

## Slide 72: History of VLIW Processors
Started with (horizontal) microprogramming
  Very-wide microinstructions used to directly generate control signals in single-issue processors (e.g., IBM 360 series)
VLIW for multi-issue processors first appeared in the Multiflow and Cydrome (in the early 1980’s)
Commercial VLIW processors from past decade
  Intel i860 RISC (dual mode: scalar and VLIW)
  Intel I-64 (EPIC: Itanium and Itanium 2)
  Transmeta Crusoe (the chip that powered Green Destiny)
  Lucent/Motorola StarCore, ADI TigerSHARC, Infineon (Siemens) Carmel
Notes: SKIP THIS

## Slide 73: Overview: VLIW Processors
Package multiple operations into one instruction
Example: VLIW processor
  One integer instruction (or branch)
  Two independent floating-point operations
  Two independent memory references
Must be enough parallelism in code to fill the available slots
Multiple Issue and Static Scheduling

## Slide 74: VLIW Processors (Static Multiple-Issue Machines)
Static multiple-issue processors (aka VLIW) use the compiler to decide which instructions to issue and execute simultaneously
  Issue packet or “bundle”
    The set of instructions that are bundled together and issued in one clock cycle—think of it as one large instruction with multiple operations
    The mix of instructions in the packet (bundle) is usually restricted—a single “instruction” with several predefined fields
      e.g., VLIW: one integer (or branch), two FP, two memory
  Performance
    Must be enough parallelism in code to fill the available slots
    The compiler does static branch prediction and code scheduling to reduce (ctrl) or eliminate (data) hazards
Notes:  Package multiple operations into one instruction

## Slide 75: VLIW Processors
Advantages
  Simpler hardware (potentially less power hungry)
  Potentially more scalable
    Allow more instructions per bundle & add more FUs
Disadvantages:
  Statically finding parallelism
  Code size
  No hazard detection hardware
  Binary code compatibility
Multiple Issue and Static Scheduling
RISC-V Code Snippet
Loop: fld f0,0(x1)
fadd.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,-8
bne x1,x2,Loop
Notes: Overview here (code from page 171 in 6th edition). We’ll do another example in more detail with MIPS-based code later but with only 2-way issue instead of … what appears to be at least 4-way issue here.
This code merely increments a vector of values in memory, starting at 0(x1) and ending at 0(x2), by a scalar in register f2.
Note: Disadvantage of statically finding parallelism? Difficult for compilers to deal with aliasing and long latencies  slow compilation times
Given that the VLIW compiler knows that bundle can have at most 2 memory refs, 2 floating-point ops, and an integer op,
… what do you notice that the compiler has done to improve the performance of the code for VLIW execution?
Loop unrolling (with a loop-unrolling factor of 7)
Significant pressure on the register file. 5 registers (f0,f2,f4,x1,x2) to 17 registers (f0,f2,f4,f6,f8,f10,f12,f14,f16,f18,f20,f22,f24,f26,f28,x1,x2)

## Slide 76: VLIW in Illustration
Characteristics
Hardware does not need to re-analyze code to detect dependences
Hardware does not perform OoO execution
Each instruction controls multiple functional units
Each instruction is explicitly parallel

## Slide 77: Static Multiple-Issue Machines (VLIW)
Profile of VLIWs
  Multiple functional units (like SS processors)
  Multi-ported register files (again like SS processors)
  Wide program bus
Example of VLIW Processor
  One integer instruction (or branch)
  Two independent floating-point operations
  Two independent memory references
Key
  Must be enough parallelism in code to fill the available slots
Notes: Disadvantages of VLIW
  Statically finding parallelism  difficult for compilers to deal with aliasing and long latencies  slow compilation times
  Code size
  No hazard detection hardware
  No binary code compatibility

## Slide 78: An Example: VLIW MIPS
Consider a 2-issue MIPS with a 2-instr bundle
Instructions are always fetched, decoded, and issued in pairs
  What happens if one instr slot is not used?
  What does the register file have to support?
  What other hardware must we add?
ALU Op (R format)
or
Branch (I format)
Load or Store (I format)
64 bits
Notes: If one instr of the pair cannot be used, it is replaced with a “no op” (nop)
Need 4 read ports and 2 write ports and a separate memory address adder

## Slide 79: An Example: VLIW MIPS
Consider a 2-issue MIPS with a 2-instr bundle
Instructions are always fetched, decoded, and issued in pairs
  If one instr of the pair cannot be used, it is replaced with a “no op” (nop)
  Need 4 read ports and 2 write ports and a separate memory address adder
ALU Op (R format)
or
Branch (I format)
Load or Store (I format)
64 bits
Notes: Assume load and stores take two cycles.

## Slide 80: A MIPS VLIW (2-issue) Datapath
Instruction
Memory
Add
PC
8
Write Data
Write Addr
Register
File
ALU
Add
Data
Memory
Sign
Extend
Add
Sign
Extend
No hazard hardware (so load-use needs explicit nop instruction(s) inserted by compiler)
Let’s say we wanted more functional units. What would need to change?
Notes: Assume forwarding hardware as necessary.
Label IF, ID, EX, MEM, WB.
What is the top mux input to the ALU doing?
What about the bottom mux inputs to the ALU?

## Slide 81: Code Scheduling Example
Consider the following loop code: lp: lw $t0,0($s1) # $t0=array element addu $t0,$t0,$s2 # add scalar in $s2 sw $t0,0($s1) # store result addi $s1,$s1,-4 # decrement pointer bne $s1,$0,lp # branch if $s1 != 0
Must “schedule” the instructions to avoid pipeline stalls
  Instructions in one bundle must be independent
  Must separate load-use instructions from their loads by one cycle
  Notice that the first two instructions have a load-use dependency, the next two and last two have data dependencies
  Assume branches are perfectly predicted by the hardware
i = n;
do {
a[i] += const;
} while (--i != 0);
Notes: i = n;
do {
a[i] += const;
} while (--i != 0);

## Slide 82: The Scheduled Code (Not Unrolled)
Four clock cycles to execute 5 instructions for a
  CPI of 0.8 (versus the best case of 0.5)
  IPC of 1.25 (versus the best case of 2.0)
  “no op” instructions don’t count towards performance !!
 | ALU or branch | Data transfer | CC
lp: | addi $s1,$s1,-4 | lw $t0,0($s1) | 1
 |  |  | 2
 | addu $t0,$t0,$s2 |  | 3
 | bne $s1,$0,lp | sw $t0,4($s1) | 4
Notes: How many registers used? 3

## Slide 83: Scheduled Code (Not Unrolled)
How many clock cycles?
How many instructions?
CPI? Best case?
IPC? Best case?
 | ALU or branch | Data transfer | CC
lp: |  |  | 1
 |  |  | 2
 |  |  | 3
 |  |  | 4
 |  |  | 5
Notes: How many registers used? 3

## Slide 84: Loop Unrolling
Loop unrolling—multiple copies of the loop body are made and instructions from different iterations are scheduled together as a way to increase ILP
Apply loop unrolling (4 times for our example) and then schedule the resulting code
  Eliminate unnecessary loop overhead instructions
  Schedule so as to avoid load-use hazards
During unrolling, the compiler applies register renaming to eliminate all data dependencies that are not true dependencies

## Slide 85: Unrolled Code Example
lp: lw $t0,0($s1) # $t0=array element
lw $t1,-4($s1) # $t1=array element
lw $t2,-8($s1) # $t2=array element
lw $t3,-12($s1) # $t3=array element
addu $t0,$t0,$s2 # add scalar in $s2
addu $t1,$t1,$s2 # add scalar in $s2
addu $t2,$t2,$s2 # add scalar in $s2
addu $t3,$t3,$s2 # add scalar in $s2
sw $t0,0($s1) # store result
sw $t1,-4($s1) # store result
sw $t2,-8($s1) # store result
sw $t3,-12($s1) # store result
addi $s1,$s1,-16 # decrement pointer
bne $s1,$0,lp # branch if $s1 != 0
Notes: What assumption have we made in unrolling this loop code?
- # of iterations is a multiple of 4
How do we fix this?
How many clock cycles?
How many instructions?
CPI? Best case?
IPC? Best case?
How many registers? 6
What is the increase in code size? Effectively, 4x

## Slide 86: Scheduled Code (Unrolled)
Eight clock cycles to execute 14 instructions for a
  CPI of 0.57 (versus the best case of 0.5)
  IPC of 1.8 (versus the best case of 2.0)
 | ALU or branch | Data transfer | CC
lp: | addi $s1,$s1,-16 | lw $t0,0($s1) | 1
 |  | lw $t1,12($s1) | 2
 | addu $t0,$t0,$s2 | lw $t2,8($s1) | 3
 | addu $t1,$t1,$s2 | lw $t3,4($s1) | 4
 | addu $t2,$t2,$s2 | sw $t0,16($s1) | 5
 | addu $t3,$t3,$s2 | sw $t1,12($s1) | 6
 |  | sw $t2,8($s1) | 7
 | bne $s1,$0,lp | sw $t3,4($s1) | 8
Notes: Is this the same number of instructions?
What’s the theoretical best if we unrolled 1000 times? (0.75, I think, l/s is full but ALU is half full)

## Slide 87: Scheduled Code (Unrolled)
 | ALU or branch | Data transfer | CC
lp: |  |  | 1
 |  |  | 2
 |  |  | 3
 |  |  | 4
 |  |  | 5
 |  |  | 6
 |  |  | 7
 |  |  | 8
Notes: Eight clock cycles to execute 14 instructions for a
  CPI of 0.57 (versus the best case of 0.5)
  IPC of 1.8 (versus the best case of 2.0)
Is this the same number of instructions?
What’s the theoretical best if we unrolled 1000 times? (0.75, I think, l/s is full but ALU is half full)

## Slide 88: What does N=14 assembly look like?
Two instructions from a scientific benchmark (Linpack) for a MultiFlow CPU with 14 operations per instruction.
Notes: Anyone know what this looks like in the Intel/AMD CPU ISA?
Think about what instruction contains multiple sub-instructions?
MMX ( single instruction, multiple data (SIMD) instruction set designed by Intel )
SSE ( streaming SIMD extensions )
AVX ( advanced vector extensions )
Here's how you operate on 8 ints at a time.
For ints, the arithmetic uses _epi32, and the load and store use the weird _si256 type, which just means one giant 256-bit block of integer data.
#include "immintrin.h"
void foo(void) { int f[8]={1,2,0,3,5,5,10,11};
  __m256i v=_mm256_load_si256((const __m256i *)&f[0]);
  v=_mm256_add_epi32(v,v);
  _mm256_store_si256((__m256i *)&f[0],v);
  iarray_print(f,8);
}

## Slide 89: Defining Attributes of VLIW
Compiler
  1. MultiOp: instruction containing multiple independent operations
  2. Specified number of resources of specified types
  3. Exposed, architectural latencies
Add
Add
Mpy
Mem
Mem
Register File
add
nop
nop
load
store
VLIW instruction =
5 independent operations
Icache

## Slide 90: Compiler Support for VLIW Processors
The compiler packs groups of independent instructions into the bundle
  Because branch prediction is not perfect, done by code re-ordering (trace scheduling)
The compiler uses loop unrolling to expose more ILP
The compiler uses register renaming to solve name dependencies and ensures no-load use hazards occur

## Slide 91: Compiler Support for VLIW Processors
While superscalars use dynamic prediction, VLIWs primarily depend on the compiler for extracting ILP
  Loop unrolling reduces the number of conditional branches
  Predication eliminates if-the-else branch structures by replacing them with predicated instructions
    We’ll cover this in a future lecture as well
The compiler predicts memory bank references to help minimize memory bank conflicts
Notes: Predication works by executing instructions from both paths of the branch and only permitting those instructions from the taken path to modify architectural state.
ONLY the instructions from the taken path can modify architectural state because they have been associated (predicated) with a predicate, which is a Boolean value used by the instruction to control whether the instruction is allowed to modify the architectural state or not.
Predication is best explained by example. Consider the C if-then-else statement and its pseudoassembly language implementation in Listing One. Each path through the assembly code requires a branch so that only the true or false leg is executed. If the branch is mispredicted, the program can incur a performance penalty. Now imagine that, instead of using a branch to control execution of the statement in Listing One, you compute Boolean values, b1 and b2, and use those Boolean values to switch on/off instructions that make up the if-then-else statement. The code might look something like Listing Two.

## Slide 92: VLIW Advantages
Advantages
  Simpler hardware (potentially less power hungry)
  Potentially more scalable
    Allow more instructions per VLIW bundle and add more FUs
Notes: Also need bigger RegFile since renaming uses programmer visible registers (not an RUU as with SS)

## Slide 93: VLIW Disadvantages
Programmer/compiler complexity and longer compilation times
  Deep pipelines and long latencies can be confusing (making peak performance elusive)
Lock-step operation, i.e., on hazard all future issues stall until hazard is resolved (hence need for predication)
Object (binary) code incompatibility
Needs lots of program memory bandwidth
Code bloat
  “No ops” are a waste of program memory space
  Loop unrolling to expose more ILP uses more program memory space
Notes: Also need bigger RegFile since renaming uses programmer visible registers (not an RUU as with SS)

## Slide 94: Branch-Target Buffer
Need high instruction bandwidth!
  Branch-Target buffers
    Next PC prediction buffer, indexed by current PC
Adv. Techniques for Instruction Delivery and Speculation

## Slide 95: Branch Folding
Optimization:
  Larger branch-target buffer
  Add target instruction into buffer to deal with longer decoding time required by larger buffer
  “Branch folding”
Adv. Techniques for Instruction Delivery and Speculation

## Slide 96: Return Address Predictor
Most unconditional branches come from function returns
The same procedure can be called from multiple sites
  Causes the buffer to potentially forget about the return address from previous calls
Create return address buffer organized as a stack
Adv. Techniques for Instruction Delivery and Speculation

## Slide 97: Integrated Instruction Fetch Unit
Design monolithic unit that performs:
  Branch prediction
  Instruction prefetch
    Fetch ahead
  Instruction memory access and buffering
    Deal with crossing cache lines
Adv. Techniques for Instruction Delivery and Speculation

## Slide 98: Register Renaming
Register renaming vs. reorder buffers
  Instead of virtual registers from reservation stations and reorder buffer, create a single register pool
    Contains visible registers and virtual registers
  Use hardware-based map to rename registers during issue
  WAW and WAR hazards are avoided
  Speculation recovery occurs by copying during commit
  Still need a ROB-like queue to update table in order
  Simplifies commit:
    Record that mapping between architectural register and physical register is no longer speculative
    Free up physical register used to hold older value
    In other words: SWAP physical registers on commit
  Physical register de-allocation is more difficult
Adv. Techniques for Instruction Delivery and Speculation

## Slide 99: Integrated Issue and Renaming
Combining instruction issue with register renaming:
  Issue logic pre-reserves enough physical registers for the bundle (fixed number?)
  Issue logic finds dependencies within bundle, maps registers as necessary
  Issue logic finds dependencies between current bundle and already in-flight bundles, maps registers as necessary
Adv. Techniques for Instruction Delivery and Speculation

## Slide 100: Review: Multiple-Issue Processor Styles
Dynamic multiple-issue processors (aka superscalar)
  Decisions on which instructions to execute simultaneously (in the range of 2 to 8 in 2005) are being made dynamically (at run time by the hardware)
  E.g., IBM Power 2, Pentium 4, MIPS R10K, HP PA 8500 IBM
Static multiple-issue processors (aka VLIW)
  Decisions on which instructions to execute simultaneously are being made statically (at compile time by the compiler)
  E.g., Intel Itanium and Itanium 2 for the IA-64 ISA – EPIC (Explicit Parallel Instruction Computer)
    128-bit “bundles” containing 3 instructions each 41 bits + 5 bit template field (specifies which FU each instr needs)
    Five functional units (IntALU, MMedia, DMem, FPALU, Branch)
    Extensive support for speculation and predication

## Slide 101: CISC vs RISC vs SS vs VLIW
 | CISC | RISC | Superscalar | VLIW
Instr size | variable size | fixed size | fixed size | fixed size (but large)
Instr format | variable format | fixed format | fixed format | fixed format
Registers | few, some special | many GP | GP and rename | many, many GP
Memory reference | embedded in many instrs | load/store | load/store | load/store
Key Issues | decode complexity | data forwarding, hazards | hardware dependency resolution | (compiler) code scheduling
Instruction flow |  |  |  | 
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
IF
ID
EX
M
WB
EX
M
WB
Notes: Pipelining helps instruction bandwidth, not instruction latency
Loop unrolling and software pipelining to help with data hazards
Dynamic branch prediction + early branch target address calculation for speculative execution

## Slide 102: Multiple Issue