## Slide 1
Chapter 2
Memory Hierarchy Design
Part 3: Case Study with POWER
Computer Architecture
A Quantitative Approach, Sixth Edition
“Ideally one would desire an indefinitely large memory capacity such that any particular … word would be immediately available. … We are … forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.”
– A. W. Burks, H. H. Goldstine, and J. von Neumann, Preliminary Discussion of the Logical Design of an Electronic Computing Instrument (1946)

## Slide 2: Acknowledgements
Thanks to many sources for slide material
  © 1990 Morgan Kaufmann Publishers, © 2001-present Elsevier
  Computer Architecture: A Quantitative Approach by J. Hennessy & D. Patterson
  © 1994 Morgan Kaufmann Publishers, © 2001-present Elsevier
  Computer Organization and Design by D. Patterson & J. Hennessy
  © 2002 K. Asinovic & Arvind, MIT
  © 2002 J. Kubiatowicz, University of California at Berkeley
  © 2006, © 2010 No Starch Press for Inside the Machine by J. Stokes
  © 2007 W.-M. Hwu & D. Kirk, University of Illinois & NVIDIA
  © 2007-2010 J. Owens, University of California at Davis
  © 2010 CRC Press for Introduction to Concurrency in Programming Languages by M. Sottile, T. Mattson, and C. Rasmussen
  © 2017, IBM POWER9 Processor Architecture by Sadasivam et al., IBM
  © 2016, © 2019 POWER9 Processor User’s Manual, IBM
  © The OpenPOWER Foundation
  © 2022, W. Feng, Virginia Tech

## Slide 3: Recall: Basic Cache Optimizations
Larger block size
  Reduces compulsory misses
  Increases capacity and conflict misses, increases miss penalty
Larger total cache capacity to reduce miss rate
  Increases hit time, increases power consumption
Higher associativity
  Reduces conflict misses
  Increases hit time, increases power consumption
Higher number of cache levels
  Reduces overall memory access time, increases complexity
Giving priority to read misses over writes
  Reduces miss penalty, increases complexity
Avoiding address translation in cache indexing
  Reduces hit time
Review Appendix B, as needed.
Notes: Caching must cope with translation of virtual address to physical address.
Common optimization: Use the page offset, i.e., the part that is identical in both virtual and physical addresses, to index the ache.

## Slide 4: Recall: Advanced Optimizations for Caching
Reduce Hit Time
  (1) Small & simple first-level $ and (2) way prediction
    Side effect: Reduce power consumption
Increase Cache Bandwidth
  (3) Pipelined $, (4) non-blocking $, and (5) multi-banked $
    Side effect: Varying impacts on power consumption
Reduce Miss Penalty
  (6) Critical word first and (7) merging write buffers
    Side effect: Little impact on power
Reduce Miss Rate
  (8) Compiler optimizations. Side effect: Reduces power consumption
Reduce Miss Penalty or Miss Rate via Parallelism
  (9) Hardware pre-fetching and (10) compiler pre-fetching
Key
  $ = cache
Notes: https://www.coursera.org/lecture/comparch/cache-pipelining-Nfcjx
Pre-fetching generally increases power consumption, primarily due to prefetched data that is unused.

## Slide 5: Recall: Avg. Memory Access Time
How to reduce the average memory access time?
  Reduce hit time
  Reduce miss rate
  Reduce miss penalty
Notes: Obvious answers:
Reduce hit time.
Reduce miss rate.
Reduce miss penalty.

## Slide 6: Recall: Cache Coherence & Performance
Summary
  Unlike details with pipelining (e.g., ILP) that only concern compiler writers, you the programmer need to acknowledge that cache coherence is going on “under the covers.” Why?
    The coherence protocol can DRAMATICALLY impact your performance!

## Slide 7: Impact of Cache Coherence in Multicore CPUs
Notes: Just changed the interleaving of memory accesses between the processing cores.
Make a quiz question with traversal pattern.

## Slide 8: Case Study: POWER Architecture
POWER8: 64-bit implementation of the POWER ISA
  Compute
    Capable of up to eight-way simultaneous multithreading (SMT)
    Enhanced branch prediction, which uses local & global prediction tables with a selector table to choose the preferred predictor
  Memory
    Block Size: 128 B
    L1 Instruction $: 32 kB, eight-way set-associative
    L1 Data $: 64 kB, eight-way set-associative
    L2 $ per Core/Chip: 512 kB / 6 MB
    L3 $ per Core/Chip: 8 MB / 96 MB
    L4 $ per Chip: 128 MB
    Enhanced prefetch with instruction speculation awareness and data prefetch depth awareness
Notes: L4: Off chip: 16 MB memory buffer chip per channel, 8 chips per socket.

## Slide 9: Case Study: POWER Architecture
 | POWER8 | POWER9 | POWER10 | Replacement?
Block Size | 128 B | 128 B | 128 B | -
L1 Instr. $ | 32 kB (8-way) | 32 kB (8-way) | 48 kB | 
L1 Data $ | 64 kB (8-way) | 32 kB (8-way) | 32 kB | Pseudo-LRU
L2 $ Core/Chip | 512 kB / 6 MB | 512 kB (8-way) | 2 MB | 
L3 $ “Core”/Chip | 8 MB / 96 MB | 10 MB (20-way) | -/120 MB | 
L4 $ Chip | 128 MB | 128 MB |  | 
Sources: IBM and 7-cpu.com
Note: POWER10 read/write bandwidth of memory and L3/L2/L1 cache is double that of POWER9.
Notes: POWER8:
362 mm2 (for 6 cores chip version), 22 nm, 15 layers, Cu, SOI,
L1 Data cache = 64 KB, 128 B/line, 8-WAY
L1 Instruction cache = 32 KB, 8-WAY
L2 cache = 512 KB per core, 128 B/line, 8-WAY
L3 local cache (Fast-L3 Region cache) = 8 MB (eDRAM), 128 B/line, 8-WAY
L3 cache = (8 MB * 5) per chip (eDRAM) consist of LOCAL-L3 from another cores, 128 B/line,
L4: Off chip: 16 MB memory buffer chip per channel, 8 chips per socket.
POWER9: 695 mm2 (for 24 cores chip version), 14 nm, 17 layers, Cu, SOI finFET. 8 billion transistors.
L1 Data cache = 32 KB, 128 B/line (2x 64-byte sectors), 8-WAY. 8 banks. Store-through (to L2 cache) policy; no allocate on store misses. Pseudo-LRU. 64-byte reload interface from the L2 cache can supply 64 bytes in every processor clock. Effective address index, real address tags (hardware fix-up on alias cases).
L1 Instruction cache = 32 KB, (4x 32-byte sectors), 8-WAY, Effective-address index, real-address tags.
L2 cache = 512 KB per core, 128 B/line, 8-WAY. 2-bank. One processor read port, two snoop read ports, and one write port per physical bank
L3 local cache (Fast-L3 Region cache) = 10 MB (eDRAM) per 2 cores, 128 B/line, 20-WAY
L3 cache = (10 MB * 12) per chip (eDRAM) consist of LOCAL-L3 from another cores, 128 B/line (2x 64-byte sector), victim cache for L2 cache and, victim cache for other on-chip L3 caches. 64-byte wide data bus to L2 for reads.
RAM: 8x DDR4
On-chip accelerators, including on-chip encryption, compression, and random number generation accelerators
Fetch: 8 instructions
Decode: 6 instructions
Dispatch: 6 instructions

## Slide 10: Case Study: POWER Architecture
POWER8 Additional Details
  62 mm2 (for 6 cores/chip version), 22 nm, 15 layers, Cu, SOI,
  L1 Instruction $ = 32 KB, 8-WAY
  L1 Data $ = 64 KB, 128 B/line, 8-WAY
  L2 cache = 512 KB per core, 128 B/line, 8-WAY
  L3 local cache (Fast-L3 Region cache) = 8 MB (eDRAM), 128 B/line, 8-WAY
  L3 cache = (8 MB * 5) per chip (eDRAM) consist of LOCAL-L3 from another cores, 128 B/line,
  L4: Off chip: 16 MB memory buffer chip per channel, 8 chips per socket.
Notes: POWER8:
362 mm2 (for 6 cores chip version), 22 nm, 15 layers, Cu, SOI,
L1 Data cache = 64 KB, 128 B/line, 8-WAY
L1 Instruction cache = 32 KB, 8-WAY
L2 cache = 512 KB per core, 128 B/line, 8-WAY
L3 local cache (Fast-L3 Region cache) = 8 MB (eDRAM), 128 B/line, 8-WAY
L3 cache = (8 MB * 5) per chip (eDRAM) consist of LOCAL-L3 from another cores, 128 B/line,
L4: Off chip: 16 MB memory buffer chip per channel, 8 chips per socket.
POWER9: 695 mm2 (for 24 cores chip version), 14 nm, 17 layers, Cu, SOI finFET. 8 billion transistors.
L1 Data cache = 32 KB, 128 B/line (2x 64-byte sectors), 8-WAY. 8 banks. Store-through (to L2 cache) policy; no allocate on store misses. Pseudo-LRU. 64-byte reload interface from the L2 cache can supply 64 bytes in every processor clock. Effective address index, real address tags (hardware fix-up on alias cases).
L1 Instruction cache = 32 KB, (4x 32-byte sectors), 8-WAY, Effective-address index, real-address tags.
L2 cache = 512 KB per core, 128 B/line, 8-WAY. 2-bank. One processor read port, two snoop read ports, and one write port per physical bank
L3 local cache (Fast-L3 Region cache) = 10 MB (eDRAM) per 2 cores, 128 B/line, 20-WAY
L3 cache = (10 MB * 12) per chip (eDRAM) consist of LOCAL-L3 from another cores, 128 B/line (2x 64-byte sector), victim cache for L2 cache and, victim cache for other on-chip L3 caches. 64-byte wide data bus to L2 for reads.
RAM: 8x DDR4
On-chip accelerators, including on-chip encryption, compression, and random number generation accelerators
Fetch: 8 instructions
Decode: 6 instructions
Dispatch: 6 instructions

## Slide 11: Case Study: POWER Architecture
POWER9 Additional Details
  695 mm2 (for 24 cores chip version), 14 nm, 17 layers, Cu, SOI finFET.
  L1 Instruction $ = 32 KB, (4x 32-byte sectors), 8-WAY, effective-address index, real-address tags.
  L1 Data $ = 32 KB, 128 B/line (2x 64-byte sectors), 8-WAY. 8 banks. Store-through (to L2 $) policy; no allocate on store misses. Pseudo-LRU. 64-byte reload interface from the L2 $ can supply 64 bytes in every processor clock. Effective address index, real address tags.
  L2 $ = 512 KB per core, 128 B/line, 8-WAY. 2-bank. 1 processor read port, 2 snoop read ports, and 1 write port per physical bank
  L3 local cache (Fast-L3 Region cache) = 10 MB (eDRAM) per 2 cores, 128 B/line, 20-WAY
  L3 $ = (10 MB * 12) per chip (eDRAM) consist of LOCAL-L3 from another cores, 128 B/line (2x 64-byte sector), victim cache for L2 cache, and victim cache for other on-chip L3 caches. 64-byte wide data bus to L2 for reads.
Notes: POWER8:
362 mm2 (for 6 cores chip version), 22 nm, 15 layers, Cu, SOI,
L1 Data cache = 64 KB, 128 B/line, 8-WAY
L1 Instruction cache = 32 KB, 8-WAY
L2 cache = 512 KB per core, 128 B/line, 8-WAY
L3 local cache (Fast-L3 Region cache) = 8 MB (eDRAM), 128 B/line, 8-WAY
L3 cache = (8 MB * 5) per chip (eDRAM) consist of LOCAL-L3 from another cores, 128 B/line,
L4: Off chip: 16 MB memory buffer chip per channel, 8 chips per socket.
POWER9: 695 mm2 (for 24 cores chip version), 14 nm, 17 layers, Cu, SOI finFET. 8 billion transistors.
L1 Data cache = 32 KB, 128 B/line (2x 64-byte sectors), 8-WAY. 8 banks. Store-through (to L2 cache) policy; no allocate on store misses. Pseudo-LRU. 64-byte reload interface from the L2 cache can supply 64 bytes in every processor clock. Effective address index, real address tags (hardware fix-up on alias cases).
L1 Instruction cache = 32 KB, (4x 32-byte sectors), 8-WAY, Effective-address index, real-address tags.
L2 cache = 512 KB per core, 128 B/line, 8-WAY. 2-bank. One processor read port, two snoop read ports, and one write port per physical bank
L3 local cache (Fast-L3 Region cache) = 10 MB (eDRAM) per 2 cores, 128 B/line, 20-WAY
L3 cache = (10 MB * 12) per chip (eDRAM) consist of LOCAL-L3 from another cores, 128 B/line (2x 64-byte sector), victim cache for L2 cache and, victim cache for other on-chip L3 caches. 64-byte wide data bus to L2 for reads.
RAM: 8x DDR4
On-chip accelerators, including on-chip encryption, compression, and random number generation accelerators
Fetch: 8 instructions
Decode: 6 instructions
Dispatch: 6 instructions