## Slide 1: Project topics for CS 4505

## Slide 2: Project Topic 1
Title: Adding support for the missing floating-point instructions in gem5 for POWER ISA
  Example: fsqrt
    floating-point instruction that computes the square root of a value
  Outcome: Robust and validated floating point arithmetic instruction support
  Input(s): floating point value in FRB register
  Output: The square root of the floating-point operand in register FRB is placed into register FRT
  Challenges:
    Functionally correct floating-point representation
      Issues: byte-swapping
    Need to handle floating-point exceptions

## Slide 3: Project Topic 2
Title: Adding support for the out-of-order execution model O3CPU for POWER ISA in gem5
  Example:
    O3CPU is supported for X86 ISA in gem5. Use X86 O3CPU as a reference and implement O3CPU for POWER.
  Outcome: Robust and validated O3CPU support
  Input(s): A benchmark suite ex. SPEC’17
  Output: Functionally correct output for the benchmark along with out of order execution
  Challenges:
    Requires significant efforts to implement and to ensure correctness
    Much harder to implement O3CPU with speculation
      Consider implementing O3CPU without speculation for baseline and then think about including speculation if time permits

## Slide 4: Project Topic 3
Title: Finding the best cache configuration for a given set of workloads
  Example:
    Search space exploration into best performing cache parameters for a given workload. Tunable parameters include cache size, number of caches (2/3/4-level hierarchy) cache associativity, cache replacement policy etc.
  Outcome: Identification of best performing cache configuration
  Input(s): A set of workloads taken from a benchmark suite ex. SPEC’17
  Output: Best performing cache configuration for each workload
  Challenges:
    Large number of tunable parameters
    Difficult to automate the evaluation process

## Slide 5: Project Topic 4
Title: Manual vectorization using VSX and MMA instructions
  Example:
    Vectorize the image convolution operation
  Outcome: Vectorized code with correct outputs
  Input(s): A set of workloads taken from a benchmark suite ex. SPEC’17
  Output: A vectorized implementation of the input code that delivers significant performance improvements over the input code
  Challenges:
    VSX/MMA kernels are tedious to write and verify